## Slide 1: SolidWorks Customization
By Brian J Lindahl, P.E., CSWP
20 Aug 2013
Burnsville, MN
Technical Summit

## Slide 2: Topics for Customization
System Options (5 to 10 minutes)
Document Options (2 minutes)
Keyboard (2 to 5 minutes)
Mouse (2 to 5 minutes)
Toolbars (2 minutes)
Menus (2 minutes)
Options (2 Minutes)
Materials Database (5 minutes)
Hole Wizard/Hole Calloutformat.txt (5 minutes)
Macros (30 to 45 minutes)
Questions (1 to 15 minutes)
SolidWorks Technical Summit 2013

## Slide 3: 1. System Options
Settings optimized for performance
I should already know if my models have errors – Don’t notify me and slow me down when saving
If I record a Macro, it will need editing to make the code usable and versatile enough to use
Option can automatically re-order FeatureTree to allow error-free rebuild. I’d rather diagnose errors first manually–the design intent may require re-ordering. Clear check
Again, I should know when errors exist. Don’t prompt me with each rebuild
If you use a Custom Property for a component description, map it to the FeatureTree here
This can only distract me from my work. News from SW can wait.
SolidWorks Technical Summit 2013

## Slide 4: 1. System Options – Performance
Clear the “High quality…” for ultimate speed settings – looks bad though
Load assemblies lightweight – know the results – especially with Feature driven component patterns
Mate animation speed is Off
No preview during open
SolidWorks Technical Summit 2013

## Slide 5: 1. System Options - Assemblies
SolidWorks Technical Summit 2013
Check “Save to external file” for (human) compatibility reasons
Consider smaller threshold for using Large Assembly Mode. Maybe 100 or 200.
Suspend automatic rebuild can be good, but you may find yourself using “<Ctrl-Q>” so much that it is counter-productive

## Slide 6: 1. System Options - View
SolidWorks Technical Summit 2013
All three are only “Wow factors”. Set to off for best performance. It is like “instant solve”

## Slide 7: 1. System Options – Backup/Recovery
SolidWorks Technical Summit 2013
It only takes one recovered crash to offset months or even years of the time it takes for the computer to make the backup files. Use it!
At the same time, don’t RELY on it. Always save any work of “value” frequently!

## Slide 8: 2. Document Properties – Image Quality
SolidWorks Technical Summit 2013
Image quality does not affect model accuracy. Image quality is how much work the graphics card does to put a picture of the model on the screen. Set to as low as possible, then when you get comfortable with what models look like, change the templates setting a bit lower still, until working “roughly” in the middle to left-of-center on the scale (industry dependant!)

## Slide 9: 3. Keyboard
SolidWorks Technical Summit 2013
SolidWorks out of the box includes about 50 - 60 pre-programmed keyboard shortcuts, some being very useful
After customization, I currently have about 28 extra keyboard shortcuts. These are at least as useful as the original keyboard shortcuts

## Slide 10: 3. Keyboard
Two ways to set Keyboard shortcut keys:
  Manually assign through Tools>Customize>Keyboard OR RMB on a menu or toolbar and Customize>Keyboard
  Copy Settings Wizard
Shortcut Key combination possibilities A-Z, 0-9, F1-F12:
  “A”
  <Shift>A
  <Ctrl>A
  <Alt>A
  <Shift><Ctrl>A
  <Shift><Alt>A
  <Ctrl><Alt>A
  <Ctrl><Shift><Alt>A
Approximately 48 * 8 = 384 programmable keyboard shortcuts!
SolidWorks Technical Summit 2013

## Slide 11: 4. M-i-c k-e-y M-o-u-s-e
Starting with SolidWorks 2010, SW supports “Mouse Gestures”, where the users can RMB click and drag across a portion of a circular ring. Sections of the circular ring display programmable buttons. Simply dragging the mouse pointer across the button initiates the command.
SolidWorks Technical Summit 2013

## Slide 12: 4. M-i-c k-e-y M-o-u-s-e
Set Mouse Gestures at Tools>Customize>Mouse Gestures
I suggest programming mouse gestures that DON’T have keyboard shortcuts. What’s the point in duplication?
Separate lists for mouse gestures exist for the 4 main environments in SolidWorks:
  Sketching
  Parts
  Assemblies
  Drawings
SolidWorks Technical Summit 2013

## Slide 13: 5. Toolbars
SolidWorks 2011 Standard has 39 built-in toolbars. Toggle visibility at Tool>Customize>Toolbars. New toolbars are generally added only by “Add-ins”
Toolbars can each be modified by adding or removing existing buttons from the pre-defined toolbars. Drag and drop icon from ‘Commands’ tab on to add/off to remove
CommandManager tabs are basically equal to Toolbars, and can be created from scratch. Drag and drop icons to/from like above
Macros toolbar is treated a bit special by ‘Copy Settings Wizard’ in that it can be isolated for Copy/Restore purposes
SolidWorks Technical Summit 2013

## Slide 14: 5. Toolbars
CommandManager: Enabled at Tools>Customize>Toolbars
When creating your own toolbar buttons, don’t be afraid to “create” icons for the new buttons:
  Cut and paste icons or screen shots into “Paint”, crop to 16 x 16 bits, save as file type .bmp.
SolidWorks Technical Summit 2013

## Slide 15: 6. Menus
Standard Menus can be customized to remove options, or restore those already removed.
To add new menu selections, Tools>Customize>Menus
  Top two selections are the new command being added
  Bottom 3 selections are the menu being added, and the command name added into the menu
Click “Add” to have “Make Normal” command added to the “Tools” menu in this picture
SolidWorks Technical Summit 2013

## Slide 16: 7. Options
Options allows full RMB menus (to eliminate “ “ from the bottom of shortcut menus) and complete icon set in Shortcuts
SolidWorks Technical Summit 2013
«

## Slide 17
8. Materials database
SolidWorks Technical Summit 2013

## Slide 18
9. Hole Wizard database
SolidWorks Technical Summit 2013
“Out of the box” standards (ANSI Inch, ANSI Metric, etc) should not be modified
Create your company “standard”, add, modify, enable or disable sizes as needed at Tools>Options>System Options>HoleWizard/Toolbox>Configure
See the presentation “Effective Use of the Hole Wizard” – at SolidWorks World Proceedings, 2008, 2009, 2010, 2011, 2012 or 2013 or www.cadspeedupllc.com – for detailed outline of modification procedure.
Support the created standard by updating the ‘calloutformat.txt’ file by adding a section with the new standard’s name

## Slide 19
Macros are programs supported and ran by calling SolidWorks functions, giving access to SolidWorks functionality, along with spreadsheet, text, database, etc, functionality of other programs installed on the machine.
Simplest macros are “Visual Basic for Applications”, or VBA code, and can be run from Tools>Macro>Run, or can be assigned a shortcut key, or a toolbar button
Higher end code is .NET compatible, using Visual Studio languages (Visual Basic, Visual C, etc.), and can be run from Tools>Macro>Run, or can be assigned to a shortcut key, or a toolbar button, and in addition can run independent of SolidWorks, or even be a stand-alone application that might launch SolidWorks from within the macro
Basically anything that is doable in SolidWorks can (or should) be programmable in a macro
10. Macros
SolidWorks Technical Summit 2013

## Slide 20
10. Macros
SolidWorks Technical Summit 2013
“Gotta-Have” macros:
Add jog to dim. ext. line
Remove jog
Set Document Precision
Set Annotation Precision
Find/open file based on file name
Synchronize SolidWorks Custom Properties or PDM fields with ERP fields (about 350 lines of code)

## Slide 21
Drive an ERP system from SolidWorks:
  Create new records in ERP when a new SW part/assembly requires an ERP Part# record
  Push BOM from SolidWorks into ERP’s BOM table
  Perform common ERP Item Maintenance (like updating a description)
  Checking Where-Used in ERP’s BOM table
  Item Search on multiple fields in combination
  (all in about 3000 lines of code and 5 or 6 forms!)
10. Macros
SolidWorks Technical Summit 2013

## Slide 22: Questions:
Contact:
Brian Lindahl, PE, CSWP
  Senior Engineer
  CAD_Speed-Up, LLC
  2105 81st Street
  Somerset, WI 54025
  brian@cadspeedupllc.com
  715-781-2881
THANK YOU!!
“Do what is good and right” Deut 6:18.